The model stepwise
of racr-mquat
name
= concept/context/non-terminal/terminal/ag-rule in the model
= currently missing feature in the model
= in the model, but not evaluated

---
The basic model
virtual root
SW
Root
root
C1
I1.a
reqComp
I1.b
S1
S2
C2
C3
I2.a
I3.a
I2.b
I3.b
CB1
R1
CB2
CB3
S3
C4
I4.a
I4.b
CB4
CB5
Software components (circles) with implementations (round rectangles) and their dependencies (arrows)
dependency specified in contract
together with NFP-constrains
maybe also parallelism/sequential
constraints for subcomponents,
e.g. C2 || C3, C2 – C3
Hardware resources (boxes) and
their subresources (lines)
provided NFPs
maybe also shared resources, e.g. NAS

---
Model += Selection
selectedimpl
I1.a
I2.b
deployedOn
Assignment of implementations to HW components (PE)

---
Model += Modes
I1.a#fast
I2.b#slow
Assignment of modes implementations to HW components (PE)
mode name is shown after the hash symbol (#)
if no mode show, the fist (and mostly the only) mode of the impl is meant

---
Model += Request
Request
MetaParameter-
(key,value)
*
Constraints
Objective
Request keeps information on
concrete values of metaparameters (list size, video resolution, particle count, …)
constraints on properties of called component (response time max 400ms, precision min 0.4, …) [optional]
objective (minimize energy, maximize precision, …) [optional, energy is default]

---
Model += Contracts and Clauses
ProvClause
I1.a#fast (
 requires C2 { p2 min 3 }
 requires C3 { p3 min 5 }
 requires PE { cpu-load max 0.5
   ram-free min 1.2*workload })
I1.a#slow ( … )
Contract defined on implementions
comprising modes for this impl
mode is a named set of clauses (either requirement or provision)
PEs have a set of properties

---
Model += Clause-Evaluation
 requires C2 { p2 comp-min
f(params) = 3 }
 requires PE { ram-free comp-min
f(params) = 1.2 * workload })
Clauses have a comparator and a value function
value function takes request-metaparameters and returns a value
comparator takes required and actual value and compares them (returning boolean)
returned value of a Property, i.e. ReturnType
target (either Comp or ResourceType)

---
Model += Clause-Evaluation
 requires C2 { p2 comp-min
f(params) = 3 }
 requires PE { ram-free comp-min
f(params) = 1.2 * workload })
Clauses have a comparator and a value function
value function takes request-metaparameters and returns a value
comparator takes required and actual value and compares them (returning boolean)
returned value of a Property, i.e. ReturnType
target (either Comp or ResourceType)
returnType

---
Model += Clause-Evaluation
 requires C2 { p2 comp-min
f(params) = 3 }
 requires PE { ram-free comp-min
f(params) = 1.2 * workload })
Clauses have a comparator and a value function
value function takes request-metaparameters and returns a value
comparator takes required and actual value and compares them (returning boolean)
returned value of a Property, i.e. ReturnType
target (either Comp or ResourceType)
comparator

---
Model += Clause-Evaluation
 requires C2 { p2 comp-min
f(params) = 3 }
 requires PE { ram-free comp-min
f(params) = 1.2 * workload })
Clauses have a comparator and a value function
value function takes request-metaparameters and returns a value
comparator takes required and actual value and compares them (returning boolean)
returned value of a Property, i.e. ReturnType
target (either Comp or ResourceType)
value function

---
Model += Clause-Evaluation
 requires C2 { p2 comp-min
f(params) = 3 }
 requires PE { ram-free comp-min
f(params) = 1.2 * workload })
Clauses have a comparator and a value function
value function takes request-metaparameters and returns a value
comparator takes required and actual value and compares them (returning boolean)
returned value of a Property, i.e. ReturnType
target (either Comp or ResourceType)
comparator