The model stepwise
of racr-mquat

---
The basic model
virtual root
root
C1
I1.a
reqComp
I1.b
S1
S2
C2
C3
I2.a
I3.a
I2.b
I3.b
CB1
R1
CB2
CB3
S3
C4
I4.a
I4.b
CB4
CB5
Software components (circles) with implementations (round rectangles) and their dependencies (arrows)
dependency specified in contract
together with NFP-constrains
maybe also parallelism
constraints for subcomponents,
e.g. C2 – C3
Hardware components (boxes) and
their structure (lines)
provided NFPs
maybe also shared resources, e.g. NAS

---
Model += Selection
selectedimpl
I1.a
I2.b
deployedOn
Assignment of implementations to HW components (PE)

---
Model += Modes
I1.a#fast
I2.b#slow
Assignment of modes implementations to HW components (PE)
if no mode show, the fist (and mostly the only) mode of the impl is meant

---
Model += Request
Request
MetaParameter-
(key,value)
*
*
Constraint
Objective
Request keeps information on
concrete values of metaparameters (list size, video resolution, particle count, …)
constraints on properties of called component (response time max 400ms, precision min 0.4, …) [optional]
objective (minimize energy, maximize precision, …) [optional]

---
Model += Contracts and Modes
Request
MetaParameter-
(key,value)
*
*
Constraint
Objective
*
ProvClause
I1.a#fast (
 requires C2 { p2 min 3 }
 requires C3 { p3 min 5 }
 requires PE { cpu-load max 0.5
   ram-free min 1.2*workload })
I1.a#slow ( … )
Contract defined on implementions
comprising modes for this impl
mode is a named set of clauses (either requirement or provision)
PEs have a set of properties